## Slide 1
Group routing continuation
Static routing and OSPF
Submission template
Group number: __________ Members: ____________________
Screenshots 1–5 • Continues Lab 050: Linux Static Routing

## Slide 2
Screenshot 1 Working static routing
Inside node: private source IP and curl to all partner websites (two or three).
Router: exact partner /24 static route and DHCP next hop.
Use real names. Keep commands, source addresses and results readable.

## Slide 3
Screenshot 2 Stale static route
Exact remote /24 remains; partner curl fails and local website still works.
Observer WAN stays up. Include identifiable partner VM powered-off image
with your SSH terminal evidence on this slide.
Use real names. Keep commands, source addresses and results readable.

## Slide 4
Screenshot 3 OSPF working
Router: partner neighbor state, OSPF remote /24 and kernel proto ospf route.
Inside node: private-source curl to all partner websites (two or three).
Use real names. Keep commands, source addresses and results readable.

## Slide 5
Screenshot 4 OSPF route withdrawal
After the 40-second dead interval, remote /24 is absent from FRR and kernel.
Remote curl fails; local website works and observer WAN stays up.
Include identifiable partner VM powered-off image with your SSH evidence.
Use real names. Keep commands, source addresses and results readable.

## Slide 6
Screenshot 5 OSPF recovery and third group
Partner restarts: neighbor, route and website return. Restore private IP if needed.
Third group: learned /24 and successful inside-node curl without manual routes.
Use real names. Keep commands, source addresses and results readable.